## Slide 1: Multiple Cars Tracking Basing on Kalman Filter
Team #13
Pengluo Wang; Kaiyu Zhang;
Shihao Luo
ECE 251B –Digital Signal Processing Ⅱ

## Slide 2: Contents
01
02
03
04
Problem
Data
Solutions
Results

## Slide 3: Problem
Background
  The automatic driving is one of the most important technical achievement, which still needs more promotion
  Implement a set of algorithm to combine car detection and tracking together, to provide convenience for car driving.
What we did
  Use different methods implement the car detecting and tracking, and add the window marking the multiple cars inside the video.
  For car detection, we choose Tensorflow Object Detection API to make detection
  After getting the information of detected cars(location and velocity), we make the prediction using Kalman Filter, and combine the prediction & measurement value as the real tracking value, to finish whole algorithm.

## Slide 4: Dataset
Video Data
  The Data we use is a set of video taken by the dashcam in front of our car, which is real and reliable.
  The Data was taken in our daily life, including different situation: No Cars, One Car, More than One Cars in the visual area.
  The cars in the video have several typical behaviors including intersection and overtaking.
（A） (B) (C)

## Slide 5: Method Introduction-Detection
Tensorflow Object Detection API
  TensorFlow Object Detection API is an open source framework built on top of TensorFlow that makes it easy to construct, train and deploy object detection models.
  To use this build-in model, we applies SSD with MobileNet, a Single-shot-detection with mobilenet architecture trained on COCO test set.
SSD - Single-Shot-Detection
  SSD algorithm is an object detection algorithm that directly predicts the coordinates and categories of the objection with bounding box.
  SSD is much faster than those traditional detection models without losing the accuracy, by adding several separate prediction filters
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 6: Method Introduction-Detection
SSD - Basic Frames
  Using a small convolutional filter to predict object categories and offsets in bounding box locations
  Using separate predictors (filters) for different aspect ratio detections
  Applying these filters to multiple feature maps from the later stages of a network in order to perform detection at multiple scales
  Train the data with ground truth boxes, which make the model can be used for detection and prediction
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 7: Method Introduction-Detection
SSD – Outcome
  This model has been trained with COCO data set, which can detect the following objects related to transportation:
Label Number | Objection
1 | Person
2 | Bicycle
3 | Car
4 | Motorcycle
5 | Bus
6 | Train
7 | Traffic Light
8 | Stop Sign

## Slide 8: Method Introduction-Detection
Flow Chart
SSD-Advantages
  High Speed
  High Accuracy
  Can be applied with low resolution and video data
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 9: Method Introduction-Detection
SSD – Outcome
  Using a test image, we have the following outcome:

## Slide 10: Method Introduction-Tracking
Kalman Filter
  Kalman Filter is a kind of adaptive filter.

## Slide 11: Intersection-over-Union（IoU）
IoU
  A parameter shows the accuracy of detection and prediction.
  Can be understood as the accuracy rate for each image
  For example:
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 12
Linear-Assignment
  One of the fundamental combinatorial optimization in order to find a maximum weight matching (or minimum weight perfect matching) in a weighted bipartite graph.
  Implemented by package sklearn in Python.
  Produce the max matching between detection and tracking box in our project. The results are stored in list matched, unmatched_detections, and unmatched_trackers.
Detection-to-Tracker Assignment
 | D1 | D2 | D3 | D4
T1 | 0 | 0 | 1 | 0
T2 | 1 | 0 | 0 | 0
T3 | 0 | 0 | 0 | 0
IoU matrix
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 13
Sequential processing
  Process each frame of the input video, implemented by package MoviePy.
  Deals with matched, unmatched_detections, and unmatched_trackers ob-tained from linear assignment of the IoU matrix for each frame.
False alarm & missed detection
  Introduce two important parameters, min_hits and max_losses: min_hits stands for the minimum number of consecutive matches to establish a tracker; max_loss stands for the maximum number of consecutive losses to delete a current track.
  Introduce a variable to discriminate false alarm and real target, a tracker is called good tracker if it has reached min_hits.
Pipeline
Notes: SSD model is based on a feed-forward convolutional network that produces a fixed-size collection of bounding boxes and scores for the presence of object class instances in those boxes, followed by a non-maximum suppression step to produce the final detections.

## Slide 14: Pipeline diagram

## Slide 15: Results - Frame

## Slide 16: Results - Frame

## Slide 17: Results - Frame

## Slide 18: Results - Frame

## Slide 19: Results - Frame

## Slide 20: Results - Frame

## Slide 21: Results - Video

## Slide 22: Reference